## Slide 1: Demo effects on the classic Amiga
Aske Simon Christensen
(Blueberry / Loonies)

## Slide 2: Overview
Introduction
The display hardware
The copper
The blitter

## Slide 3: Amiga 500
Launched in 1987
7MHz Motorola 68000, 512kB RAM
Custom chips for graphics, sound, disk, etc.

## Slide 4: Now vs. then
GeForce GTX 780: 5 TFLOPS peak
  At 1920 x 1080, 60 FPS
  40000 ops / pixel / frame
Amiga 500: 7 MHz, ≥4 cycles / op
  At 320 x 256, 50 FPS
  0.4 ops / pixel / frame

## Slide 5: Effect: Dots
From ”Desert Dream” by Kefrens, 1993

## Slide 6: Effect: Sine Dots
From ”World of Commodore” by Sanity, 1992

## Slide 7: Effect: Dot Tunnel
From ”Interference” by Sanity, 1993

## Slide 8: Effect: Dot Landscape
From ”Arte” by Sanity, 1993

## Slide 9: Bitplanes
0100110111110101 0011011010101010 101010101010
1010101101101101 1001011110101000 101001010000
0000111110111011 1110000011110111 011101011111
1101001111011101 1011101110101110 110010000001
0010111100001010 1111111000010100 111111001011
10101
(21)
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Output color:

## Slide 10: Six bitplanes
Extra half-brite (EHB):
  Second set of 32 colors is darker version
Dual playfield (DPF):
  8 + 8 colors from odd / even bitplanes
Hold and modify (HAM):
  Select one of 16 colors, or
  Duplicate color from previous pixel with new R, G or B value

## Slide 11: Playfield offset
Screenshot from ”Lemmings” game by DMA Design

## Slide 12: Effect: Interference
From ”Mesmerized” by Pure Metal Coders, 1990

## Slide 13: Effect: Directional Light
From ”Desert Dream” by Kefrens, 1993

## Slide 14: Electron beam
h-blank
scanline
h-blank
scanline
h-blank
scanline
scanline
h-blank
scanline
scanline
v-blank

## Slide 15: Playfield offset in detail
Leading modulo
Shift
Trailing modulo
Vertical skip

## Slide 16: Effect: Vertical Bars
From ”Overdose” by Delight, 1991

## Slide 17: Effect: Motion Blur
From ”Hardwired” by Crionics, 1991

## Slide 18: The Copper
Co-processor with two instructions
  MOVE: Write value to hardware register
  WAIT: Wait for raster position
Copper list
Starts execution at every v-blank

## Slide 19: Split screen
Picture ”Elements of Green” by Prowler

## Slide 20: Effect: Copper Rainbow
From ”Copper Master” by Angels, 1990

## Slide 21: Effect: Copper Bars
From ”Desert Dream” by Kefrens, 1993

## Slide 22: Effect: Kefrens Bars
From ”Copper Master” by Angels, 1990

## Slide 23: Effect: Wavy Checkerboard
From ”Desert Dream” by Kefrens, 1993

## Slide 24: Effect: Copper Balls
From ”Desert Dream” by Kefrens, 1993

## Slide 25: Effect: Stretched Texture
From ”Arte” by Sanity, 1993

## Slide 26: Effect: Stretched Image
From ”Desert Dream” by Kefrens, 1993

## Slide 27: The Blitter
00001111110000001111100
000011001110001100111011110
0101010101010101010101010101010
Source A
Source B
Source C
110
111 | 110 | 101 | 100 | 011 | 010 | 001 | 000
1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
0101010101011110000101011011110
Dest D
A shift
B sh
Minterms

## Slide 28: Cookie Cut
Source A
Source B
Source C
Dest D
Mask
Image
Screen
Result
(A and B) or ((not A) and C)

## Slide 29: Effect: Bobs
From ”Seeing is Believing” by Anarchy, 1991

## Slide 30: Effect: Shade Bobs
From ”Hardwired” by Crionics, 1991

## Slide 31: Effect: Chaos Zoomer
From ”Bananamen” by Stellar, 1993

## Slide 32: Blitter filling
From right to left, switch between 0 and 1 on each 1
(Inverse: XOR with itself shifted one bit to the left)

## Slide 33: Effect: Filled Balls
From ”Interference” by Sanity, 1993

## Slide 34: Blitter Line Drawing
Solid lines
One pixel per scanline

## Slide 35: Effect: Filled Vector
From ”Seeing is Believing” by Anarchy, 1991

## Slide 36: Effect: Glenz Vector
From ”Hardwired” by Crionics, 1991

## Slide 37: Effect: Vertical Filling
From ”World of Commodore” by Sanity, 1992

## Slide 38: Effect: Plasma
From ”Overdose” by Delight, 1991

## Slide 39: Effect: Sine Plasma
From ”Arte” by Sanity, 1993

## Slide 40: Effect: Raster Tunnel
From ”Interference” by Sanity, 1993

## Slide 41: List of demos
Copper Master by Angels, 1990
Mesmerized by Pure Metal Coders, 1990
Overdose by Delight, 1991
Seeing is Believing by Anarchy, 1991
Hardwired by Crionics, 1991
World of Commodore by Sanity, 1992
Desert Dream by Kefrens, 1993
Interference by Sanity, 1993
Bananamen by Stellar, 1993
Arte by Sanity, 1993

## Slide 42: The End
?